## Slide 1
Forecasting Solar to Plan the Site Battery
DKASC Alice Springs · Assessment 3 Technical Demonstration
Abhisek Tamang
S396739
Data Engineer
Sarin Uprety
S394012
Data and Feature Engineer
Uttam Shrestha
S396560
Project Lead
Yogesh Basnet
S394043
Modelling and Visualisation Lead
PRT661 Data Science Practice · Charles Darwin University · Semester 2, 2026 · Group 4

## Slide 2
2
Overview: the problem we are solving
Abhisek
PRT661 · Group 4 · Assessment 3
The site
DKASC Alice Springs: a solar array and, since 2024, a site battery (354 kWh, measured from its own data).
The data
Master Meter 1 data every 5 minutes from 2008 to 2025 (1.77 million rows) and site telemetry data for 2024 and 2025 (battery, solar, demand, and grid).
The decision
Each night: how much cheap off peak grid energy should the battery store for tomorrow's expensive evening peak?
Generation history at the site (A2, Figure 1)

## Slide 3
3
Objectives: from A2 to A3
Abhisek
PRT661 · Group 4 · Assessment 3
Delivered in A2
Data pipeline from 19 raw extracts to a 30 feature hourly store
Forecasts of 1 h and 24 h ahead using gradient boosting outperform three baselines
80% prediction intervals, but at 24 h they only covered 70.6% of hours in the latest test period.
The actual battery decision was not yet modelled.
A3 objectives
1
Make the uncertainty credible: an 80% range that actually encompasses 80% of the values.
2
Model real site and battery from telemetry
3
Make the forecast a nightly battery decision and quantify the value.
4
Deliver it through Jira tasks, branches and reviewed pull requests

## Slide 4
4
Updated system architecture
Abhisek
PRT661 · Group 4 · Assessment 3
Two data sources
Master meter 1 for forecast, site telemetry 2024 and 2025 for the battery.
Stages 1 to 5 from A1 and A2
acquisition, storage, processing, features, models
New A3 layer (blue)
Interval calibration, site and battery model, dispatch simulation
Honest status
Planned for A4: dashboard, scheduled runs and retraining

## Slide 5
5
A2 recap: the data pipeline
Abhisek
PRT661 · Group 4 · Assessment 3
1,767,903
rows of 5 minute data in Master Meter 1
19
406 column names reconciled, yearly extracts profiled.
6
The register wraps repaired and validated against power with 99.7% accuracy.
30
hourly features, leakage safe
8
Quality gates with thresholds
Parquet
columnar store at the 5 minute and hourly level

## Slide 6
6
Workflow: data to decision, and how we work
Sarin
PRT661 · Group 4 · Assessment 3
A: notebooks 01 – 06 execute sequentially; only the previous notebook writes to its respective notebook.
The blue boxes are new to A3: notebook 06 and the saved forecasts from 05
B: All changes are done using the same 7 steps as for Jira task to merge
Example: SCRUM-44 to 47, branch, pull request #2, merged

## Slide 7
7
Implementation progress at A3
Sarin
PRT661 · Group 4 · Assessment 3
16
A3 tasks in Jira Sprint 3
PR #2
A3 analysis merged into main
6 of 8
epics complete or on track

## Slide 8
8
A2 recap: models and the open problem
Sarin
PRT661 · Group 4 · Assessment 3
Model | 1 h MAE | 1 h R² | 24 h MAE | 24 h R²
Gradient boosting | 3.61 kW | 0.980 | 6.96 kW | 0.913
Seasonal naive | 7.74 kW | 0.887 | 7.74 kW | 0.887
Persistence | 13.90 kW | 0.866 | 7.74 kW | 0.887
Climatology | 11.07 kW | 0.889 | 11.07 kW | 0.889
Mean of four walk forward folds, 2019 to 2025
Carried into A3
70.6%
of daylight hours inside the 24 h 80% interval, latest test period 2024 to 2025 (target 80%)
The interval was too narrow: in 10 trials the interval was correct only 7 times but in 10 trials it had 80% confidence. A battery planning based on this would be overconfident.

## Slide 9
9
A3 Part A: calibrating the forecast intervals
Sarin
PRT661 · Group 4 · Assessment 3
Monthly daylight coverage, raw (grey) vs calibrated (blue)
Method: Rolling Adaptation for Conformalised Quantile Regression
80.1% · 80.0%
daylight coverage 1h and 24h for all four folds, target 80%
Fixed 3929 forecasts where the low edge was above the high edge
Rolling conformal calibration: expand or contract over the past 30 days of errors
Only uses data known at the moment, no look ahead
Latest period, 24 h: 70.6% before, 79.3% after
Every fold now 79.3% to 81.0%

## Slide 10
10
A3 Part B: the site, its battery, and data drift
Uttam
PRT661 · Group 4 · Assessment 3
demand = solar + grid + battery
The energy balance test corrected the sign of all meters (96% of hours within 2 kW)
354 kWh
battery capacity via telemetry
115 kW
charge and discharge power
82.8%
Round trip efficiency in real cycles.
Data drift, end of February 2024
The site was reconfigured: site solar divided by Master Meter 1 dropped from 2.21 to approximately 1.1. Analysis begins from 1 March 2024 and the scale used is K = 1.135 (correlation 0.995 after that).

## Slide 11
11
A3 Part C: the nightly battery decision
Uttam
PRT661 · Group 4 · Assessment 3
Chart: Apr 2024-Aug 2025, Saving against no battery.
| Battery as actually operated | Store surplus solar only | Always fill overnight | Forecast plan | Perfect foresight
Saving vs no battery (%) | 9.8 | 17.3 | 19.6 | 22.3 | 25.3
Illustrative time of use tariff: $0.15 off peak, $0.25 shoulder, $0.40 peak, $0.07 feed in
At 22:00 every night
battery space minus tomorrow's forecast solar surplus = grid energy to buy tonight
$3,419
saved beyond the best rule with no forecast
47%
of the benefit perfect foresight would give

## Slide 12
12
Demonstration of the current system
Uttam
PRT661 · Group 4 · Assessment 3
Jupyter · notebook 06
calibration table, example week (Figure 14), final KPI table
GitHub · pull request #2
commits with SCRUM keys, notebooks, figures, diagrams in the repo
Jira · Sprint 3
A3 tasks with owners and status

## Slide 13
13
Technical challenges and how we solved them
Yogesh
PRT661 · Group 4 · Assessment 3
Crossed interval edges
Problem: Went low edge on high edge in 3,929 forecasts, primarily at night.
Fix: Re-order the two sides, the median remains the same.
Overconfident intervals
Problem: In the most recent time period, 24 h range covered 70.6% rather than 80%.
Fix: Rolling conformal calibration (there: 79.3%, overall: 80.0%)
Data drift
Problem: Solar ratio reduced by half from end of February 2024 due to site reconfiguration.
Fix: Start in March 2024, scale fitted on March only
Unknown signs, logger outages
Problem: Meters are not specifying direction of positive, SOC read 0 in 7% of hours.
Fix: Energy balance test corrected for sign; excluded outage hours.

## Slide 14
14
What is the limiting factor
Yogesh
PRT661 · Group 4 · Assessment 3
Chart: What's holding the battery plan back?
| Our forecasts (median plan) | Perfect solar, our demand | Our solar, perfect demand | Both perfect
Share of perfect foresight benefit (%) | 41 | 52 | 85 | 100
Swaps by one piece at a time, based on perfect information, using the median plan (41%). The caution selected on 2024 is 47% identical to slide 11.
The weak link is "demand"
Perfect demand increases plan to 85%, perfect solar to 52%
Caution barely matters
Chosen on 2024, tested on 2025: 48% to 50% for caution 0 to 1
The larger the battery, the greater the value
Forecast gain over rules: 2.2 at half size, 3.9 at double

## Slide 15
15
Future work before A4
Yogesh
PRT661 · Group 4 · Assessment 3
1
Better demand forecast
weekday and weekend patterns, temperature
2
Optimiser instead of a rule
plan charging and discharging together
3
Store more solar
113.6 MWh was cheaply exported rather than stored
4
Drift monitoring and retraining
Automatically detects changes, such as February 2024.
5
Final report and dashboard
Week 12: A4 professional report

## Slide 16
Summary
80%
calibrated intervals that mean what they say
354 kWh
The battery is modelled using its own data.
22.3%
saving with a forecast planned battery
GitHub github.com/Uttam1618/PRT661-solar-forecasting
Jira uttamshrestha1618.atlassian.net, project SCRUM
Thank you